GB

USER MANUAL

1. Safety Instructions

- Please keep this User Manual for future reference. If you sell the unit to another user, be sure that he also receives this instruction booklet.

- Unpack and check the unit carefully that it has not been damaged during transport before using the unit.

- Before operating, ensure that the voltage and frequency of power supply match the power requirements of the unit.

- The unit should be connected to a main socket outlet with a protective earth connection

- The unit is for indoor use only in a dry location.

- The unit must be installed in a location with adequate ventilation, at least 0.5m from adjacent surfaces. Be sure that no ventilation slots are blocked.

- Disconnect mains power before fuse replacement or servicing.

- Replace fuse only with the same type.

- Make sure there are no inflammable materials close to the unit during operation.

- Use safety cable when fixing this unit.

- In the event of serious operating problem, stop using the unit immediately.

- Never try to repair the unit by yourself. Repair carried out by unskilled people can lead to damage or malfunction. Please contact the nearest authorized technical assistance center and always use the same type of spare parts.

- Do not touch any wires during operation as high voltage might be causing electric shock.

- The product is for decorative purposes only and not suitable as a household room illumination.

DISCONNECT DEVICE

Where the MAINS plug or an appliance couple is used as the disconnect device, the disconnect device shall remain readily operable.

| 2. Specifications |  |
| --- | --- |
| Power supply ............................................................................... | 220-240Vac 50/60Hz |
| Consumption......................................................................................................... | 25W |
| Laser power ................................................................. | Red : 100mW / Green : 30mW |
| RGBWA LED BALL + WHITE STROBE |  |
| Dimensions .................................................................................... | 200 x 150 x 140mm |
| Weight .................................................................................................................. | 1.2kg |

3. Installation

The unit should be mounted via its screw holes on the bracket. Always ensure that the unit is firmly fixed to avoid vibration and slipping while operating. Always ensure that the structure to which you are attaching the unit is secure and able to support a weight of 10 times of the unit’s weight. Also always use a safety cable that can hold 12 times the weight of the unit when installing the fixture.

The equipment must be fixed by professionals at a place where is out of the reach of people and where nobody can pass by or under it.

4. Operation

The unit can work either automatically, follow the rhythm of the music via the built-in microphone on the rear panel or be controlled via the supplied remote control.

Plug the unit into an appropriate mains outlet that supplies the required voltage for the unit. Press the ON/OFF switch on the remote control.

Press the MODE button to select between automatic or music controlled operation. Increase /reduce sensitivity of music-controlled operation via the SEN+/SEN- buttons.

Press FLASH button to activate the strobe and increase the flash speed via the SPEED+/- buttons. Press LASER button to activate the laser. Select the color and the speed via the COLOR and SPEED buttons

Press LED to activate the Astro light effect. Select the color red, green, blue or white via the Red, Green, Blue, White and Amber buttons. Press JUMP to jump from one color to the other. Press PULSE to change slowly the color. Press STROBE to let the ASTRO work like a strobe. Select the operating speed via the MOTOR SPEED button.